QIRC / A Class Object for PyQt5 / https://github.com/nutjob-laboratories/qirc
Version 0.0140

# Summary
The QIRC class provides a multi-threaded Internet relay chat (IRC) client for use with PyQt programs.

To use QIRC, understanding IRC and the IRC protocol is a necessity. QIRC is designed to be low level, meaning its interface is influenced by the protocol itself; QIRC can be hard to understand if you don't understand the underlying protocol.

The IRC protocol is defined in a series of RFC documents:

- RFC 1459
- RFC 2812
## Requirements
Other than PyQt5, QIRC uses only modules in the Python standard library. To use SSL/TLS to connect to IRC servers, however, the pyOpenSSL library must be installed. To install this library via the Python package installer, pip, execute this command:

pip install pyOpenSSL

QIRC uses the following modules from the standard library:

- sys
- time
- socket
- collections
- ssl (only if it is available)

# Methods
	QIRC(**kwargs) / Any of the keywords available with the configure() method can be used here.
None	configure(**kwargs) / Configures the IRC client. / Keyword Type Default Description / server String "" The server the IRC client will connect to. / port Integer 6667 The port the IRC client will connect to. / password String None The password needed to connect to the IRC server (if required). / encoding String "utf-8" What string encoding to use with the server. / ssl Boolean False Set to True to use SSL/TLS to connect to the IRC server. / verify_hostname Boolean False Set to True to verify the IRC server's host name (requires ssl to be set to True). / verify_certificate Boolean False Set to True to verify the IRC server's certificate (requires ssl to be set to True). / nickname String "qircclient" The nickname the IRC client will use. / alternate String "qirc_client" The nickname the IRC client will try to use if the first choice is already taken. / username String "qircclient" The username the IRC client will use. / realname String "qircclient" The "real name" the IRC client will use. / flood_protection Boolean True Set to False to turn off flood protection. / flood_protection_send_rate Float 1.5 If flood_protection is set to True, messages will be sent to the server at a rate of one message every X seconds, with X equal to the value set here.
None	start() / Connects the IRC client to the IRC server.
None	stop() / Disconnects the IRC client from the IRC server and terminates the client's thread.
None	privmsg(String target, String message) / Sends a PRIVMSG to the currently connected IRC server.
None	join(String channel, String key=None) / Sends a JOIN command to the currently connected IRC server.
None	part(String channel, String message=None) / Sends a PART command to the currently connected IRC server.
None	quit(String message=None) / Sends a QUIT command to the currently connected IRC server, disconnects from the IRC server, and kills the thread that the QIRC instance is using.
None	send(String message) / Sends a raw message to the currently connected IRC server. This method allows users of this class to send commands that are not otherwise supported. The data is sent to the server unchanged, other than being properly encoded and delimited (as documented in RFC 1459).

# Signals
Most signals pass a dictionary to the function they are connected to. Unless otherwise noted, all dictionary values are strings. Signal names follow this pattern:
- Signal names that start with server_ are for notifications or events that refer to the connected server or server information.
- Signal names that start with message_ are for incoming messages.
- Signal names that start with user_ are for user notifications or information.
- All other signal names are for infrequent or unique events; their names follow no pattern.
None	server_connect(Dictionary data) / Emitted when the IRC client connects to the IRC server. The data dictionary contains three keys: / client – The QIRC instance that emitted the signal / server – The IP or host name of the server connected to / port – Integer: The port on the server connected to
None	server_register(Dictionary data) / Emitted when the IRC client successfully registers with the IRC server. The data dictionary contains three keys: / client – The QIRC instance that emitted the signal / server – The IP or host name of the server connected to / port – Integer: The port on the server connected to
None	server_motd(String data) / Emitted when the IRC client receives the message of the day from the IRC server.
None	server_hostname(String data) / Emitted when the IRC client receives the server's hostname.
None	nick_collision(Dictionary data) / Emitted when the nickname the IRC client tries to register with is already taken. The IRC client will try nicknames until it finds one that is not taken (these can be set with the configure() function). The data dictionary contains three keys: / client – The QIRC instance that emitted the signal / old – The invalid nickname / new – The new nickname
None	message_all(Dictionary data) / Emitted when the IRC client receives a PRIVMSG from the server. The data dictionary contains five keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the message sender / host – The username and host of the message sender / target – The channel or user the message was sent to / message – The message
None	message_public(Dictionary data) / Emitted when the IRC client receives a PRIVMSG sent to a channel the client is in. The data dictionary contains five keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the message sender / host – The username and host of the message sender / target – The channel message was sent to / message – The message
None	message_private(Dictionary data) / Emitted when the IRC client receives a PRIVMSG sent directly to the client. The data dictionary contains five keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the message sender / host – The username and host of the message sender / target – The IRC client's nickname / message – The message
None	message_action(Dictionary data) / Emitted when the IRC client receives a CTCP action PRIVMSG. The data dictionary contains five keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the message sender / host – The username and host of the message sender / target – The channel or user the message was sent to / message – The message
None	server_ping(Dictionary data) / Emitted when the IRC client receives a PING from the server. The IRC client automatically responds to the server; this just is a notification that a PING has been received. The data dictionary contains three keys: / client – The QIRC instance that emitted the signal / server – The IP or host name of the server connected to / port – Integer: The port on the server connected to
None	tick(Integer uptime) / Emitted once a second while the IRC client is connected to the server. The uptime integer contains the length of time the IRC client has been connected, in seconds.
None	user_part(Dictionary data) / Emitted when the IRC client receives a PART message from the server. The data dictionary contains five keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the user leaving the channel / host – The username and host of the user / channel – The channel the user is leaving / reason – The reason the user left (or an empty string)
None	user_join(Dictionary data) / Emitted when the IRC client receives a JOIN message from the server. The data dictionary contains four keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the user joining the channel / host – The username and host of the user / channel – The channel the user is joining
None	user_quit(Dictionary data) / Emitted when the IRC client receives a QUIT message from the server. The data dictionary contains four keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the user quitting IRC / host – The username and host of the user / reason – The reason the user quit (or an empty string)
None	user_nick(Dictionary data) / Emitted when the IRC client receives a NICK message from the server. The data dictionary contains four keys: / client – The QIRC instance that emitted the signal / nickname – The old nickname of the user changing their nickname / host – The username and host of the user / new – The user's new nickname
None	user_list(Dictionary users) / Emitted when the IRC client receives a NAMES message from the server. The users dictionary contains five keys: / client – The QIRC instance that emitted the signal / channel – The name of the channel the user list belongs to / users – A Python list containing all users in the channel. Each entry in the list can either contain a nickname with status prefixes, or a user's nickname (with status prefixes), username, and host in nickname!username@host format.
None	user_invite(Dictionary data) / Emitted when the IRC client receives a INVITE message from the server. The data dictionary contains four keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the user sending the channel invite / host – The username and host of the user / channel – The channel
None	user_oper(Dictionary data) / Emitted when the IRC client is granted operator status by the IRC server. The data dictionary contains three keys: / client – The QIRC instance that emitted the signal / server – The IP or host name of the server connected to / port – Integer: The port on the server connected to
None	server_error(Dictionary data) / Emitted when the IRC client is sent an error message by the IRC server. The data dictionary contains four keys: / client – The QIRC instance that emitted the signal / code – Integer: The RFC error code / target – List: The target(s) the error pertains to / reason – The error's explanation text
None	user_whois(Dictionary data) / Emitted when the IRC client is sent WHOIS data from the server (in response to a WHOIS command). The data dictionary contains nine keys: / client – The QIRC instance that emitted the signal / nickname – The nickname of the user / username – The username of the user / host – The host of the user / privileges – Any privileges the user has / server – What server the user is connected to / idle – Integer: how long the user user has been idle, in seconds / signon – Integer: when the user connected to the server (UNIX timestamp) / channels – List: what channels the user is in (with status prefixes)

# Attributes
String	server	The server the IRC client is connected to.
Integer	port	The port the IRC client is connected to.
String	password	The password used to connect to the IRC server.
String	nickname	The nickname the IRC client is currently using.
String	alternate	The alternate nickname the IRC client was set to use.
String	username	The username the IRC client is using.
String	realname	The "real name" the IRC client is using.
String	encoding	What string encoding the IRC client is using.
Boolean	ssl	True if the IRC client is connected to the server via SSL/TLS, and False if otherwise.
Integer	uptime	How long the IRC client has been connected to the server, in seconds.
List	motd	The server's message of the day.
String	hostname	The server's hostname. This will be set to "Unknown" until the server notifies the IRC client what its hostname is; this will be set to its correct value after the server_hostname signal is emitted.
String	software	What software the server is running. This will be set to "Unknown" until the server notifies the IRC client what software it's running; this will be set to its correct value after the server_hostname signal is emitted.
socket object	socket	The socket object the IRC client is using for connectivity.